## Slide 1: Detector Modularity for RICH Upgrade
RICH upgrade meeting, 10.11.2010
Stephan Eisenhardt
University of Edinburgh
Motivation
Photon Detectors
Module Layout
Active Area
MaPMT Families
Input Parameters
Choices
Results
Conclusions
follow-up to presentation
from 15.10.2008
linked back from the agenda

## Slide 2: Motivation
To get a handle on the questions:
  how many photon detector tubes will be used in the upgraded RICH?
  what is the active area?
  how does a semi-realistic module of NxN MaPMT tubes looks like?
Developed a model to calculate the parameters of a module from specifications and to fill a designated detector plane with modules:
  calculations done in a spreadsheet, that:
    allows for quick parameter changes and adaptations to gauge their effect
    documents which parameters and choices go into the model
  with later optimisation of choices / correction of parameters and update of the calculations is quickly done
  the current version of the spreadsheet is attached to the agenda (its certainly not perfect, but a start to put the optimisation on a common and transparent footing)

## Slide 3: Regarded Photon Detectors
R7600: MaPMT, metal channel dynodes
  C12 (6+6 cross plate anodes): geometrical parameters only, unusable for RICH
  M16 (4x4 pixel anode): geometrical parameters only, unusable for RICH
  M64 (8x8 pixel anode): as in the 2000 proposal & -2003 studies
  M64 (8x8 pixel anode): updated calculation
R8900: MaPMT, metal channel dynodes
  C12 (6+6 cross plate anodes): geometrical parameters only, unusable for RICH
  M16 (4x4 pixel anode): geometrical parameters only, unusable for RICH
  M64 (8x8 pixel anode): hypothetical calculation, not commercially available
R11265: MaPMT, metal channel dynodes
  M64 (8x8 pixel anode): hypothetical calculation, not commercially available
H9500: flat-panel PMT, metal channel dynodes
  M256 (16x16 pixel anode): updated calculation
Data sources in spreadsheet made transparent by colour coding:
  Hamamatsu datasheet/information, derived, measured, assumed/guessed values

## Slide 4: Principle Module Layout
Outline of elements in a module: schematic only – not to scale:
  Photon detector body:
  as from specs
  Photon detector margin:
  upper limit from specs
  Mu-metal thickness:
  sheet thickness
  Mu-metal margin:
  needed due to fabrication
  precision when welding sheets
  Margin for modules:
  either from mu-metal margin
  just on one side = half the margin
(used 2008/now)

## Slide 5: Principle Module Layout
Outline of elements in a module: schematic only – not to scale:
  Photon detector body:
  as from specs
  Photon detector margin:
  upper limit from specs
  Mu-metal thickness:
  sheet thickness
  Mu-metal margin:
  needed due to fabrication
  precision when welding sheets
  Margin for modules:
  or as extra margin
(used in 2000
proposal)

## Slide 6: Active Area
Hamamatsu quotes a ‘total’ active area:
  e.g. for R7600: 18.1x18.1mm2 in a 25.7x25.7mm2 housing → fraction = 0.496
We need to work with the effective active area:
  need to account for inefficiencies between the rows/columns of pixels
  Hamamatsu only quotes gaps between anodes
  e.g. for R7600: gap size 0.3mm
  form our measurement we found an effective
  gap size of 0.2mm for the photoelectron
  collection efficiency
  as there are numerous gaps its size has
  a significant effect on the effective active
  area
  e.g. for R7600:
  gap size 0.3mm: eff. active area = 0.388
  gap size 0.2mm: eff. active area = 0,422
phe collection efficiency
scan across MaPMT pixels in steps of 0.1mm

## Slide 7: MaPMT Families
What are the differences between the MaPMT families?
  as far as I understand...
R7600 → R8900: slim window mount
  new window mount developed for the
  flat-panel PMT applied to the MaPMT
  allows for larger total active area
  my assumption: the R7600 metal-channel
  dynode structure is just scaled up to cover the larger area
→ R11265: ... (I’m doing an educated guess here)
  it has a total active area similar to the R8900, i.e. the new window mount
  (confirmed by a photograph which I saw of this tube, but didn’t get my hands on)
  Hamamatsu also quotes:
  a smaller gap size of the anodes: 0.1mm
  and the photoelectron collection efficiency increased from 0.8 (R7600) to 0.9
  that is consistent with a new design of the metal-channel dynode structure which minimises the effective gap size to about 0.1mm (TBC by measurement!)
R7600:
conventional
mount
Window
R8900:
flat-panel
mount

## Slide 8: Input Parameters
Geometry:
  housing margin total active area gap size
  R7600-pww-C12 25.7mm ±0.5mm 22.0mm 0.2mm
  R7600-pww-M16 25.7mm ±0.5mm 18.1mm 0.2mm
  R7600-pww-M64 25.7mm ±0.5mm 18.1mm 0.3mm (2000 proposal)
  R7600-pww-M64 25.7mm ±0.5mm 18.1mm 0.2mm (measured)
  R8900-pww-C12 26.2mm +0.0mm -0.5mm 23.5mm 0.2mm
  R8900-pww-M16 26.2mm +0.0mm -0.5mm 23.5mm 0.2mm
  R8900-pww-M64 26.2mm +0.0mm -0.5mm 23.5mm 0.2mm
  R11265-pww-M64 25.6mm ±0.5mm 23.0mm 0.1mm (tbc)
  H9500-pww (M256) 52.0mm ±0.3mm 49.0mm 0.2mm
  (pww = photocathode & window option, important for Photon Detection Efficiency)
Data sources in spreadsheet made transparent by colour coding:
  Hamamatsu datasheet/information, derived, measured, assumed/guessed values

## Slide 9: Input Parameters
Lenses:
  assume coverage of housing
  assume demagnification factor to project
  total active area to housing area
Mu-metal shielding:
  prototype made for R7600 with grid build
  from 0.9mm thick sheets and
  0.2mm precision (probably to either side...)
  in 2000/2003 proposal: assumed
  only 0.5mm sheet thickness necessary
  and no margin...
  2008/now conservative approach:
  0.9mm sheet thickness
  0.5mm margin to either side of sheet
Extending from Photo cathode
20 mm and 13 mm
Thickness: 0.9 mm
Precision: 0.2 mm
3x3 MaPMTs
Quartz lenses

## Slide 10: Choices
Input so far defines the module size and active area fraction, together with:
  choice of 4x4 MaPMT structure (1024 channels) or 2x2 FP-PMT structure
  choice of module margin:
    either half of mu-metal margin (used 2008/now)
    or full extra margin (as on 2000/2003 proposal)
Photondetection area to cover:
  target: 3.3m2 as in current RICH: RICH2/RICH1 = 1.5/1
  without Aerogel: RICH1 * 0.x
  with the fraction 0.x needed to cover the gas radiator
    0.7 as given by Clara’s email (used here now)
    0.45 as in LoI draft (not yet regarded, but easy to calculate)
How to cover the area:
  option 1: use only fully equipped modules and exceed required area (used here)
  option 2: use also partially equipped modules at the edges (2000/2003 proposal)
  plenty of room for optimisation (not done!)

## Slide 11: Results
Calculated parameters per tube:
  pixel size eff.active area
  on bare on lens on bare on lens
  tube surface tube surface
  2000/2003 proposal:
  R7600-pww-M64 2.00mm 2.84mm 0.388 0.781
  new calculations: (with smaller gap size)
  R7600-pww-M64 2.09mm 2.96mm 0.422 0.851
  R8900-pww-M64 2.76mm 3.08mm 0.712 0.884
  R11265-pww-M64 2.79mm 3.10mm 0.759 0.940
  H9500-pww (M256) 2.84mm 3.01mm 0.783 0.881

## Slide 12: Results
Calculated parameters per module:
  module edge eff.active area
  length with lenses without lenses
  2000/2003 proposal:
  R7600-pww-M64 108.8mm 0.698 0.346
  new calculations: (with smaller gap size and conservative mu-metal grid)
  R7600-pww-M64 113.8mm 0.695 0.345
  R8900-pww-M64 113.8mm 0.750 0.603
  R11265-pww-M64 113.4mm 0.767 0.619
  H9500-pww (M256) 109.8mm 0.790 0.702

## Slide 13: Results
Calculated parameters per RICH:
  modules used tubes used
  modules needed for 3.3m2
  RICH1 RICH2 RICH1*0.7 R1+R2 R1*0.7+R2
  2000/2003 proposal:
  R7600-pww-M64 92.5 126.5 3504
  111.5 167.25
  new calculations: (with smaller gap size and conservative mu-metal grid)
  R7600-pww-M64 104 160 72 4224 3712
  102 153 71
  R8900-pww-M64 104 160 72 4224 3712
  102 153 71
  R11265-pww-M64 104 160 72 4224 3712
  103 154 72
  H9500-pww (M256) 112 170 80 1128 1000
  110 164 77

## Slide 14: Conclusions
Model developed to transparently calculate for RICH Upgrade:
  module geometry
  active area fraction
  need for MaPMT tubes
Flexible in choice of parameters / extendable as new information comes in
Covered MaPMT families to the best of available knowledge:
  the two most interesting M64 options are not yet commercially available
Deciding of coverage of active area with modules and partial equipment of modules at the edges needs further optimisation
... feel free to play with the model... (.xlsx file uploaded to the agenda)