## Slide 1
Advanced Implantation Detector Array (AIDA)
HISPEC/DESPEC meeting 26 February 2018
presented by
Tom Davinson
on behalf of the AIDA collaboration
(Edinburgh – Liverpool – STFC DL & RAL)
Tom Davinson
School of Physics & Astronomy
The University of Edinburgh

## Slide 2
AIDA Support Stand
https://www2.ph.ed.ac.uk/~td/AIDA/Information/information.html
AIDA snout assembly – manufacture in progress
AIDA support 8cm x 8cm & 8cm x 24cm DSSSDs
awaits integration with FATIMA/DEGAS
→ snout length
→ FEE64 – DSSSD cable length
→ plastic detector?
Services routing
ac mains power
2x Gbit Ethernet
cooling water
White Rabbit
etc
all overhead?
Temperature controlled cooling water
  +20 ºC

## Slide 3
Current situation:
White Rabbit provides common timestamp to all experiments
Data from each experiment are sent to MBS DAQ
Data flows are merged by MBS DAQ (see next slide)
Data are written to Tape Library in MBS format
Data from Tape Library have to be sorted – new sort program needed!
AIDA
FATIMA
DEGAS
MBS
Tape Library
RooT file
Writes data to
Missing!
Online merge
AIDA + MBS data flow
Expect AIDA data rate ~2-4Mb/s

## Slide 4
As of 16 February 2018
Tested AIDA with White Rabbit-supplied timestamps – OK!
Tested sending AIDA data blocks to MBS – OK!
  AIDA data is placed in 64 KB buffer
  AIDA Buffer event is created when buffer is full / timeout
  AIDA Buffer event contains data with White Rabbit timestamp
  AIDA Buffers are time-ordered
Regular MBS Event
AIDA 64kb Buffer MBS event
Regular MBS Event
Regular MBS Event
Regular MBS Event
Note - AIDA data is time ordered , AIDA+ MBS data is not!
AIDA + MBS tests

## Slide 5
Data size
2x Checks
Event type - AIDA
4x MBS event timestamp = timestamp 1
Data payload, e.g.
Strip, energy, timestamp 1
Strip, energy, timestamp 2
Strip, energy, timestamp 3,
….
FFFF FFFF
0000 0000 (until end of buffer)
Data size
2x Checks
Event type (e.g. FATIMA)
4x MBS event timestamp
Data payload, e.g.
Detector 1 + Energy 1
Detector 2 + Energy 2
Detector 3 + Energy 3
FFFF FFFF
Regular MBS event
Aida Buffer MBS Event
AIDA data cf. MBS events
AIDA uses GREAT data format STFC DL edoc504
http://npg.dl.ac.uk/documents/edoc504/edoc504.html

## Slide 6
Valencian
Merger Tool
(J.Agramunt et al.)
AIDA
LuckyDoll (RIKEN; Phong)
AIDAsort (Edin./CMU; Chris/Oscar, Neerajan)
BigRIPS
Anaroot (RIKEN; Matsui)
BRIKEN
BRIKEN sort(?) (Valencia; Jorge, Alvaro)
AIDA RAW DATA
BigRIPS RAW DATA
BRIKEN RAW DATA
AIDA
Root TTree
BigRIPS
Root TTree
BRIKEN
Root TTree
BRIKEN Data Analysis Pipeline
Online Data Analysis
Courtesy Alfredo Estrade Vaz & Jorge Agramunt
TTrees time ordered

## Slide 7
Acknowledgements
AIDA collaboration
http://www2.ph.ed.ac.uk/~td/AIDA/welcome.html
BRIKEN collaboration
https://www.wiki.ed.ac.uk/display/BRIKEN/Home
RIKEN Nishina Centre for Accelerator-Based Science
S.Nishimura, G.Kiss, K.Matsui, P.Vi et al.