# General Risk Assessment

# Form RA1

(Refer to Notes for Guidance before completing this form)

| School Assessment No: |  |
| --- | --- |
| Title of Activity: | Senior Honours Project – Quantum Physics: Illusion or Reality? |
| Location(s) of Work: | JCMB 5308 |
| Brief Description of Work: Six week undergraduate (senior honours) project undertaken in the Nuclear Physics (NP) research group laboratory. This project uses NaI(Tl) scintillator detectors with Photomultiplier Tubes (PMTs) to observe correlated -rays from a 22Na radioactive source shielded by lead bricks. |

Hazard Identification: Identify all the hazards; evaluate the risks (low / medium / high); describe all existing control measures and identify any further measures required.  Specific hazards should be assessed on a separate risk assessment form and cross-referenced with this document.  Specific assessments are available for hazardous substances, biological agents, display screen equipment, manual handling operations and fieldwork.  See http://www.ed.ac.uk/schools-departments/health-safety/risk-assessments-checklists/risk-assessments for details.

| Hazard(s) | Present Risk Evaluation L/M/H | Control Measures (i.e., alternative work methods / mechanical aids / engineering controls, etc.) | Risk Evaluation after control L/M/H |
| --- | --- | --- | --- |
| Lone working Out of hours working Radioactive sources Lead shielding High voltage | M M L L L | Undergraduate students to be supervised by academic staff and NP group technician Undergraduate students are only permitted laboratory access during office hours on weekdays Students may only handle sealed radioactive sources <370kBq activity. Use handling tongs, inverse square law and shielding to minimise exposure. Exercise caution handling lead blocks used for shielding to avoid mechanical injuries. Wash hands following the handling of lead blocks. Students are not permitted to connect/disconnect HV cabling or to remove the covers/enclosures of equipment supplying/using HV. | L L L L L |

*Continue on separate sheet if necessary

Engineering Controls: Tick relevant boxes

| Guarding |  | Extraction (LEV) |  | Interlocks |  | Enclosure |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Other relevant information (incl. testing frequency if appropriate): |

Personal Protective Equipment (PPE): Identify all necessary PPE.

| Eye / Face |  | Hand /Arm |  | Feet / Legs |  | Respiratory |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Body (clothing) |  | Hearing |  | Other (Specify) |
| Specify the grade(s) of PPE to be worn: |
| Specify when during the activity the item(s) of PPE must be worn: |

Non-disposable items of PPE must be inspected regularly and records retained for inspection

# Persons at Risk: Identify all those who may be at risk.

| Academic staff | x | Technical staff | x | P’Grad students |  | U’Grad students | x |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Maintenance staff |  | Office staff |  | Cleaning staff |  | Emergency personnel |  |
| Contractors |  | Visitors |  | Others |  |  |  |

Additional Information: Identify any additional information relevant to the activity, including supervision, training requirements, special emergency procedures, requirement for health surveillance etc.

Assessment carried out by:

| Name: | Dr Thomas Davinson | Date: 1 June 2013 |  |
| --- | --- | --- | --- |
| Signature: |  | Review Date: 31 May 2014 |  |